SC822通讯协议
v0.0.0.3
协议格式:
头+数据包+CRC8
头
Offset	Size	Field	Type	Description
0	8	Flag	Constant	F2
8	8	Address	Number	7:1为Device发送，0为PC主机发送
16	4	Token	Number
22	12	Size	Number
32	8	Check	Number	XOR

Offset是以bit来计算

Token
Value	Description
0000	请求Size
0001	允许Size
0010	PING
0011	TokenPack
1101	数据错误,重传
1110	忙
1111	数据包太大

数据包
获取长数据
命令包
Offset	Size	Field	Type	Description
0	1	Command	Constant	0x39
1	3	Address	Number
4	2	Size	Number
6	n	Data	Number

应答包
Offset	Size	Field	Type	Description
0	1	Command	Constant	0xF9 / 0xB9
1	2	Size/Return	Number	操作返回
3	n	Data	Number

设置长数据
命令包
Offset	Size	Field	Type	Description
0	1	Command	Constant	0x7A
1	3	Address	Number
4	2	Size	Number
6	n	Data	Number

应答包
Offset	Size	Field	Type	Description
0	1	Command	Constant	0xBA
1	2	Return	Number	操作返回

设置位
命令包
Offset	Size	Field	Type	Description
0	1	Command	Constant	0x3C
1	3	Address	Number
4	1	Bit	Number
5	1	Data	Number

应答包
Offset	Size	Field	Type	Description
0	1	Command	Constant	0xBC
1	2	Return	Number	操作返回

擦除FLASH
命令包
Offset	Size	Field	Type	Description
0	1	Command	Constant	0x3D
1	3	Address	Number

应答包
Offset	Size	Field	Type	Description
0	1	Command	Constant	0xBD
1	2	Return	Number	操作返回

设置时间
命令包
Offset	Size	Field	Type	Description
0	1	Command	Constant	0x46
1	5	Data	Number

应答包
Offset	Size	Field	Type	Description
0	1	Command	Constant	0x86
1	2	Return	Number	操作返回

获取时间
命令包
Offset	Size	Field	Type	Description
0	1	Command	Constant	0x07

应答包
Offset	Size	Field	Type	Description
0	1	Command	Constant	0xC7
1	5	Data	Number

添加用户
命令包
Offset	Size	Field	Type	Description
0	1	Command	Constant	0x48
1	13	Data	Number

应答包
Offset	Size	Field	Type	Description
0	1	Command	Constant	0x88
1	2	Return	Number	操作返回

删除用户
命令包
Offset	Size	Field	Type	Description
0	1	Command	Constant	0x10
1	4	UserID	Number

应答包
Offset	Size	Field	Type	Description
0	1	Command	Constant	0x10
1	2	Return	Number	操作返回

获取日志
命令包
Offset	Size	Field	Type	Description
0	1	Command	Constant	0x0A
1	4	LogID	Number

应答包
Offset	Size	Field	Type	Description
0	1	Command	Constant	0xCA/0x8A
1	2	Size/Return	Number
3	n	Data	Number

设置下载点
命令包

Offset	Size	Field	Type	Description
0	1	Command	Constant	0x0B
1	4	LogID	Number

应答包
Offset	Size	Field	Type	Description
0	1	Command	Constant	0xCA
1	2	Return	Number	操作返回